# PC-ALE Setup with RTL-SDR for quiet scanning
Rob VK3ARL, 07/07/2021

This setup is currently quite complicated, and is pretty developmental. The idea is to avoid abusing the relays in a Xiegu G90 (or any other non-ALE transceiver) by using an RTL-SDR or similar SDR receiver to do high-speed scanning, and only switching in the G90 when required for TX (sounding and calling).
Out of the box, PC-ALE v1.08 beta 32 does not have an easy way to separate these functions.
I put together an AutoHotkey script which watches for certain words to appear in the 'status bar' in the PC-ALE program (the bar at the bottom of the Windows application). The status bar is a relatively convenient, albeit unconventional, way to read the current requirements of PC-ALE, particularly for when it is about to transmit. I am not a coder, and I don’t know how to achieve this function using a more conventional programming language.
This method of constantly watching the status bar works, but you do need to make sure that "Listen before TX" is checked. Increasing the 'PTTD ms' to around 300 also seems to give the system more time to react to status bar changes.
Ideally, you need a T/R switch on a single multiband antenna. If not available, two antennas are required, one for RTL-SDR and one for the G90. Care should be taken to avoid overloading the receiver RTL-SDR.
While not fully tested, the tuner on the G90 should be able to be set on each band of use, checked, then the tuner left on while under CAT control. This should protect the G90 from high SWR, and shouldn't overuse the tuner relays.
At this stage, CAT control cannot replace VOX for PTT on the transceiver. It is possible, however the ideal timings are not really able to be pulled from just the status bar text, so this is not implemented at this stage.

The setup is as follows:

1. Plug the CAT control cable into the G90, the USB audio cable into the CE-19 (the external data module used with the G90), then the CE-19 into the G90.
2. Set the G90 to use VOX (required), and Input to "Line". See the Xiegu G90 groups.io forum for heaps of info on this rig. So far, this is the same setup as that required for FT8 and similar data modes.
3. Connect the RTL-SDR to the PC.
4. Use “com0com” to create a pair of virtual COM ports.
5. Use a virtual audio cable program, and set up one virtual cable (I use VBCable).
6. Open SDRSharp with an RTL-SDR plugged in, and use the CalicoCAT plugin to expose control to one side of the virtual COM ports.
7. Output the SDRSharp audio to "CABLE Input".
8. Open PC-ALE, open "MIL-STD-188-141 Options" and set the radio type to "KENWOOD" (the type of radio that CalicoCAT mimics). Point the "CAT Comm Port" to the OTHER SIDE of the virtual pair used for CalicoCAT in SDRSharp.
9. Set up the Soundcard settings in PC-ALE to listen on the "CABLE Output" and to transmit on the audio out (speakers) of the USB audio adapter. The G90 then uses VOX for PTT.
10. Download and install AutoHotkey.
11. Download Hamlib. I have version 3.3.
12. Place the TXChecker.ahk script into the Hamlib executables folder (“bin\”).
13. Run the TXChecker.ahk script by double clicking, and enter the COM port of the G90. This can be found in the Windows Device Manager.
14. In PC-ALE, start scanning. SDRSharp should be scanning, using the RTL-SDR. When the script is triggered, the transceiver should change frequency to the current PC-ALE frequency before PC-ALE starts to transmit.